## Slide 2
Seapix :
an innovative multibeam multiswath echosounder
for water column and seabed analysis
Guillaume Matte, Didier Charlot, Olivier Lerda, Trung-Kien N'Guyen, Vinicius Giovanini, Maxence Rioblanc and Frédéric Mosca
Ixblue Sonar System Division, ENSICAEN
David Vincentelli

## Slide 3
Sonar Imaging at iXblue
Seapix
Station Based Imaging
Backscatter Imaging
Conclusion

## Slide 4
Sonar Imaging at iXblue
1

## Slide 5
SEABED
MAPPING
SUB-BOTTOM
PROFILING
BOTTOM
IMAGING
WATER COLUMN
MONITORING
Sonar Imaging at iXblue : from near surface to subbottom

## Slide 6
Seapix
  Multibeam/Multiswath Echosounder
2

## Slide 7
Requirement Specifications
  Volumetric scanning of the water column
  Bathymetry up to 400m
  Target detection -35dB up to 200m
  Limited size (Φ< 50cm)
  Bathymetry IHO 1a
  Market
  Fisheries
  Context : Sustainable Policy and Selectivity
  Evaluation of fisheries resources in collaboration with scientific (vessel of opportunity )
  Challenges
  Tradeoff hardware cost / level of performances
  from single beam to multibeam interpretation
Project Specifications, Development
Seapix
SEAPIX Research&Development
  start in 2008
  2 FUI (Optipêche/Tactipêche, Ifremer)
  1 RAPID (MUSE, Ensta)

## Slide 8
System Specifications
Seapix
Specifications | 
Size | 480mmx180mm
Weight | 60/40 kg
Power consumption | 200W (500W Peak)
Number of transducers | 2x 64 Rx and Tx
Max Depth | 20m
Beam Stabilization | On transmit and receive
Frequency | 150khz
Bandwith | 10khz (7.5cm res.)
Modulation | CW or FM
Beam number | 64 beams
Transmit Power | 1kW
Beam Steering | +/-60° for/aft port/starboard
Transmit Swath width | 120 °x 1.6°

## Slide 9
Sonar Head
Seapix
Impedance Matching
Transducers
Receiver Analog Filters
Emission Power
Emission and reception Digital signal processing
Communication, configuration and Power Supply management, Gyrostabilization
Analogic
Digital
Ethernet
Acoustic
MEMS

## Slide 10
System Architecture
Seapix
Onboard Power Supply
(230Vac/ 24Vdc )
Beam Former Processor Unit
Power
Ethernet and command
Ethernet
Underwater Cable (Ethernet + Power)
Sonar
Head
Interface Unit
Viewer Processor Unit
Sonar Room
Deck
Navigation data and external MRU (optional)
NMEA

## Slide 11
Key features
  2D/3D Bathy
  2D/3D Backscatter
  2D/3D Echograms
  Multiple Echogram
  TS/SV Analysis
  HAC format (EchoView,Movies3D)
Software
Seapix
845 m !

## Slide 12
Bathymetry , ENSTA (2015) :
  IHO order 1a with MEMS
Detection Level
  Noise Level , 24 dB re 1μPa/Hz
  SV -60dB , 200m
Performances
Seapix
BaraPemdez, June 2014, scale SV [-60dB,-18dB], central beam

## Slide 13
Multiple Swath Imaging
Seapix
Versatile Configuration
User defined insonification
scenario
CW/FM
Switch Rx/Tx antenna
Steering angle interval
and increment

## Slide 14
Volume 120° x 120°
7cm radial resolution
1.6°x1.6° up to 1.6°x3.2° angle resolution
Downward Looking Configuration
Seapix
Port/Starboard
scanning
Fore/Aft
scanning

## Slide 15
Station Based Imaging
3

## Slide 16
Seapix is fixed on barge
Bathymetry area ~ 1200m² at 10m depth
Bathymetry
Station Based Imaging
Seapix
deployed leg

## Slide 17
Bathymetry
Station based imaging
Exploiting antenna reversibility to improve the reliability of bottom detections. Artefacts are removed by using virtual phases

## Slide 18
Backscatter Imaging
4

## Slide 19
Horizontal Forward Looking
Conventional Bathymetry&Imagery
Longitudinal
Multiple Imaging Modes
Backscatter Imaging

## Slide 20
Conventional Imagery Mode
Backscatter Imaging

## Slide 21
Forward Looking Imaging
Backscatter Imaging
Forward Looking Imaging:
Specular reflection suppressed
Higher shadows contrast
.
Vertical Imaging:
Specular reflection
Bad contrast at nadir
.

## Slide 22
Longitudinal Mode
Backcatter Imaging
Longitudinal Imaging Mode:
 Full BS profil vs Incidence Angle

## Slide 23
Seafloor Classification Results
Backscatter Imaging
Mode Longitudinal
Mode Transversal
Sand
Posidonia sparse
PosidoniaDense

## Slide 24
Conclusion
5

## Slide 25
Seapix reversible mills cross configuration enables an innovative use of signals recorded from perpendicular and tilted swathes
The first application example presented was the ability to build a bathymetry from a static position without the need of pan-and-tilt mechanical interface
The second application example concerned a unique bottom classification method using both longitudinal and transversal swathes.
MultiBeam/MultiSwath System
Conclusion