## Slide 1: Development of a low-cost multi-sensor platform for recording shallow water dephts
By sarah Diederichs
Wednesday 15.11.2017
HYDRO 17 Rotterdam

## Slide 2: Motivation

## Slide 3: Table of content
Basic Information
Theoretical Work-flow – From Measurement to Map
Market Analysis
System Assembly
Test run
Conclusion and Outlook

## Slide 4: Basic Information
OpenSeaMap
  The free natical chart, launched 2009
  Close cooperation with GEBCO (water depths between 100 and 10.000 meters)
Definition shallow water area
  Purpose for hobbyist or smaller vessels
    Range: 1 and 20 meters
  International Hydrographic Organization
    Shallower than 100 metres
 Accuracy specifications for this depth range (IHO Special Order)
 | 1 meter depth | 10 meter depth | 20 meter deoth
Maximum allowable THU 95% Conficence level | 2 m | 2 m | 2 m
Maximum allowable TVU 95% Conficence level | +- 0.25 m | +- 0.26 | +- 0.29

## Slide 5: Theoretical Work-flow (1#3)
Instrumentation

## Slide 6: Theoretical Work-flow (2#3)
The measurement – Data acquisition
  Normally the data is logged during a sailing trip or during work on a vessel
  Autonomously working sensor platform
    Without a great expense by chance
    Only towing the system to the vessel
Data transmission OpenSeaMap
  Account creation (Email address and password)
  Input Meta data
  Raw data upload

## Slide 7: Theoretical Work-flow (1#2)
Postprocessing steps by OpenSeaMap

## Slide 8: Market Analysis (1#2)
Bodyboard as sensor platform
Wireless „Fish Finder“ as echo sounder
Arduino board Mega 2560 as Microcontroller
High Selectivity Super Het Receiver receivies the signals

## Slide 9: Market Analysis (2#2)
Neo-6M GPS receiver
OpenSeaMap Hardware: Data Logger

## Slide 10: System Assembly (1#6)
Interfaces and level standards
  Used protocols: TTL, RS232 and RS422
   need of converters
GPS module (Neo–6M)
  Configuration with „u-center – GNSS evaluation software for Windows“ from U-blox company:
    Baud rate: 4800 Bd
    NMEA-0183 format

## Slide 11: System Assembly (2#6)
Sonar Sensor Investigation - Fish Finder
  Decoding and transmission of the data
  Oscilloscope and the software Saleae Logic 1.2.11 is used to determine the structure of the received signals

## Slide 12: System Assembly (3#6)
Sonar Sensor Investigation - Fish finder

## Slide 13: System Assembly (4#6)
Fish Finder – decoding
  Two possibilities to decode the signal and to filter out the depth
    1) Depth value decoded in the first 16 bit block (Manchester)
    2) Reflection time analogue to signal duration after the synchronisation pulse
      Time of the low signal after synchronisation pulse  analogue to the time of the acoustic pulse in water
      Depth equation
Programming with an Arduino and the IDE interface software (PC)
  Scanning for synchonisation pulse (fixed duration
  Check if the pulse appeared inside the time frame for sonar returns
  Timer usage  low signal duration till first rising edge
  Depth calculation
  Serial Output NMEA-0183 depth data string

## Slide 14: System Assembly (5#6)
Connection to the OpenSeaMap Data Logger
  Via patch cable (network cable)
  Wire configuration
  Connection link: converter (from TTL to RS232) between GPS and Sonar and the data logger

## Slide 15: System Assembly (6#6)
Fish Finder fixed to the board with same orientation as the Data Logger, having identical movements

## Slide 16: Test case scenario
Test area: pond with 2 meters water depth
The System has been dragged over the water surface for 2 1/2 hours
Results:
  Sufficient sampling of depths & GPS postions)
  Data written in correct NMEA-0183 format to SD card
  Depths mainly measured correctly
  But also errors reg. water depths exist:
    No depth data
    Multiple depths caused by reflections
  Open SeaMap data uploads without any issue

## Slide 17: Conclusion and Outlook
Conclusion
  Bad accuracies of the Fish Finder  Advise of using another sonar sensor
  Also not quite clear how a hobbyist should assemble such system without suffcient prior knowledge
  Nevertheless, it has to be said that the task which was to develop a multi-sensor platform with low-cost components has been fulfilled.
Outlook
  Great potential: further processing and improvement by plausibility checks and suppressing of worse measures
    Improving of the build up and programming part
    Better sensors
  Test run (up to 20 m depth)  possible better accuracies.

## Slide 18: Thank you for your attention!