## Slide 1: Multiple Data Deliveries from one Data Source the Multibeam System
Ellen Stuifbergen

## Slide 2: Multiple Deliverables from the MB
    Bathymetry data
    SSS data
    Snippet data
    Bottom Classification data
    Water Column data
    Multi detect data
    Pipeline data (5 points)

## Slide 3: Multiple Deliverables
  Collect different data sets in one survey
  Saves boat and survey time
  Is this possible?

## Slide 4: Bathymetry

## Slide 5: Depth information

## Slide 6: Scattering
Sound striking bodies in the water and being reflected from:
  Surface, bottom and land
  Organic particles
  Marine life
  Bubbles
  Temperature variations

## Slide 7: Backscatter
Of all energy scattered, only intensities registered by the receiver is coined as “backscatter”.
Seabed Backscatter
Specular reflection
scatter
scatter
Notes: First let’s look at the phenomenon ‘Scatter’

## Slide 8: Types of Backscatter
SeaBat creates 3 types of backscatter:
  Side Scan backscatter
  Snippets backscatter
  Water column backscatter
Water column Backscatter
Volume scatter
Seabed Backscatter
Specular reflection
scatter
scatter

## Slide 9: Backscatter types

## Slide 10: SeaBat Backscatter type 1): Side scan

## Slide 11: SeaBat Backscatter type 2): Snippets

## Slide 12: Snippets Data
A Snippet is the series of amplitude values in the signal reflected from a beam‘s footprint on the seafloor.

## Slide 13: How are snippets (automatically) determined?
(very) old method: fixed snippet window
  Cannot cope with dynamic environments
  Larger data records (7008) with less added value
New method: automatic snippet window
  7k and T-series (7028 record)
  Aims 1) full bottom coverage across the swath and 2) smaller files sizes
?
samples against beam angle

## Slide 14: Automatic snippet window – flat seabed
Beam (n)
Beam (n-1)
Beam (n+1)
Bottom detection @ sample (n-1)
Bottom detection @ sample (n)
Bottom detection @ sample (n+1)
Snippet window
time samples
Window = (Sn+1 – Sn) + (Sn – Sn-1)

## Slide 15: Automatic snippet window – target on seabed
Beam (n)
Beam (n-1)
Beam (n+1)
Bottom detection @ sample (n-1)
Bottom detection @ sample (n)
Bottom detection @ sample (n+1)
Snippet window
time samples
Window = (Sn+1 – Sn) + (Sn+1 – Sn)

## Slide 16: Differences Sidescan and Snippets
Snippets
Distance/Range same as Bathy data
Position of beam exactly known from Bathy data
No Bottom detection = No Snippets data
Sidescan
Watercolumn
Shadows show information

## Slide 17: Snippets Backscatter
SeaBat 7101
Teledyne PDS

## Slide 18: Depth information

## Slide 19: Snippets Backscatter for Feature Detection

## Slide 20: Bottom characterization using Snippets

## Slide 21: Influences to backscatter
Roughness
Loss of energy
Require some chaotic scattering to return in the receive direction
Frequency dependent
Grain size, shells
Water column
Seafloor
Seabed Backscatter
scatter
scatter
Hardware:
Source level
Gain
Transmit and receive beam pattern
Ceramic sensitivity
Pulse Length/Type
Angular Response
Grazing Angle
90
0
BS (dB)
-50
-10
gravel
sand
mud
Specular reflection
Impedance
Sediment density and velocity
Large impedance contrast will give strong backscatter. E.g. air bubbles
Sub-bottom terms
Sediment attenuation
Biological life, bubbles
Attenuation
Spreading
Objects in the water

## Slide 22: Can we account for all this? We try ….
Roughness
Loss of energy
Require some chaotic scattering to return in the receive direction
Frequency dependent
Grain size, shells
Hardware:
Source level
Gain
Transmit and receive beam pattern
Ceramic sensitivity
Pulse Length/Type
Angular Response
Grazing Angle
90
0
BS (dB)
-50
-10
gravel
sand
mud
Impedance
Sediment density and velocity
Large impedance contrast will give strong backscatter. E.g. air bubbles
Sub-bottom terms
Sediment attenuation
Biological life, bubbles
Attenuation
Spreading
Objects in the water
Seabed Backscatter
scatter
scatter
Specular reflection
HW/SW gains
???
Correct for angular response in Software.
Normalized Backscatter

## Slide 23: Conclusion: Not all Backscatter is created equal
The case for Normalized Backscatter

## Slide 24: SeaBat T50 Normalized Backscatter (NBS)
Generic parameter sets established for the transmitter and receiver beam patterns, source level, ceramic sensitivity, and gain.
Backscatter is normalized to actual dB value so it can be used for repetitive mapping purposes or modelling.
Normalized backscatter is available for SeaBat T50

## Slide 25: Harbour Survey

## Slide 26: Harbour Survey
SeaBat T50-P Normalized Backscatter
Acquisition: Teledyne PDS
Processing: Teledyne CARIS

## Slide 27: Salmon Fish farm
26 m
26 m
Satellite imagery

## Slide 28: Salmon Fish farm - Bathymetry
SeaBat T50-P
Acquisition: Teledyne PDS
Processing: Teledyne CARIS

## Slide 29: Salmon Fish farm - Backscatter
SeaBat T50-P
Acquisition: Teledyne PDS
Processing: Teledyne CARIS

## Slide 30
Goa, India – T50 Normalized Backscatter
SeaBat T50-P
Acquisition: Teledyne PDS
SeaBat T50-P
Acquisition: Teledyne PDS
Processing: Teledyne PDS

## Slide 31
Goa, India – T50 Normalized Backscatter
SeaBat T50-P
Acquisition: Teledyne PDS
Processing: Teledyne PDS

## Slide 32
Goa, India – T50 Normalized Backscatter
SeaBat T50-P
Acquisition: Teledyne PDS
Processing: Teledyne PDS

## Slide 33
SeaBat T50 & Teledyne PDS
Standard Snippets Backscatter
Waterdepth ~300-400m

## Slide 34
SeaBat T50-P Normalized Backscatter
Acquisition: Teledyne PDS
Processing: Teledyne CARIS

## Slide 35
SeaBat T50-P Normalized Backscatter
Acquisition: Teledyne PDS
Processing: Teledyne CARIS

## Slide 36: SeaBat Backscatter type 3): Water Column Backscatter
Also known as: Full backscatter; Imagery; Beam Data
All intensities above the digitised bottom represent the water column backscatter

## Slide 37
Water Column

## Slide 38
Water Column Data
Notes: Compressed Water Column:
Reduces data volume significantly by intelligently removing data…
No samples below the sea floor detections (reduce by ~40%)
Convert to dB and remove 8 least significant bit (reduce by ~40%)
Remove phase information (reduce by ~40%)
Downsample by factor x (reduce by at least 50%)

## Slide 39: Applications of Water Column data
Wreck surveys
Gas vents
Sediment plumes
Oil spills
Marine mammal monitoring
Multidetect

## Slide 40: Multidetect
Bottom detection and digitalisation of intensity in beam
Up to 5 detections per beam
Detects details in the water column

## Slide 41: Multi-Detect Turbine Data

## Slide 42: Multi detect on Bridge Pillar

## Slide 43: Pipe Detection
Pipe position automatically determined by detection algorithm
Pipe displayed on User Interface
Steering of beams to pipe
Pipe adjacent depths calculated
Mean seabed depths calculated
Export in S7K data
  Top of Pipe
  Adjacent markers
  Mean seabed markers
Free spans may be calculated

## Slide 44: Feedback to Bottom Detection
Detection algorithm initially calculates top of pipe positions
BDA searches for detections in vicinity of pipe
Pipe detection algorithm automatically matches pipe position
Top of Pipe position is exported in 7k record as a 5 points file
Pipe position for next ping is initialised from previous pings

## Slide 45: Summary
Data from one multibeam system is more than only bathymetry data.
Backscatter delivers invaluable information for target detection, seabed characterization, habitat mapping
Possible to collect data at the same time
New Normalized Backscatter allows for improved consistency for repetitive mapping.
SeaBat T50 offers Normalized Backscatter and Compressed Water Column backscatter.

## Slide 46: Thank you Questions? You can also visit our booth L4

## Slide 48
SeaBat T50-P Compressed WC
QPS Fledermaus Mid-Water

## Slide 49: What’s that Nadir striping?
Grazing angle θ
Few samples (low res)
But strong specular
Many samples (high res)
Weak specular
τ pulse length

## Slide 50
MBES
phase
time
time
What’s that Nadir striping?
Few samples (low res)
But strong specular
Many samples (high res)
Weak specular
Notes: The geometry of the sonar used to map the seabed generates signals of quite different characteristics whether it is pointing straight down or off to the side.

## Slide 51: Water Column: Backscatter Time Series Mapped

## Slide 52: Tips For Snippets Backscatter Acquisition (1)
Snippets data is centred around the bottom detection so settings to ensure good bottom detection is key.
Do not over gain (7125), i.e reach saturation.
CW gives best snippets quality
Run straight lines, doe not use infill's or cross lines in the mosaic
(if not using Normalized Backscatter:) Keep constant settings. Find the right power/gain/pulse/abs/spread settings and change only if in a different survey block (ie. Not throughout a line).

## Slide 53: Automatic snippet window – flat seabed
Beam (n)
Beam (n-1)
Beam (n+1)
Bottom detection @ sample (n-1)
Bottom detection @ sample (n)
Bottom detection @ sample (n+1)
Snippet window
time samples
Window = (Sn+1 – Sn) + (Sn – Sn-1)

## Slide 54: Automatic snippet window – target on seabed
Beam (n)
Beam (n-1)
Beam (n+1)
Bottom detection @ sample (n-1)
Bottom detection @ sample (n)
Bottom detection @ sample (n+1)
Snippet window
time samples
Window = (Sn+1 – Sn) + (Sn+1 – Sn)

## Slide 55: Automatic snippet window – no neighbouring beam
Beam (n)
Beam (n+1)
Bottom detection @ sample (n)
Bottom detection @ sample (n+1)
Snippet window
time samples
Window = (Sn+1 – Sn) + (Sn+1 – Sn)